## Slide 1: TEKATHON-5.0- 2026
Problem Statement ID – 26168
AI-ML based Intelligent Dead Reckoning system for seamless navigation
Theme – Miscellaneous • PS Category – Software
Organization – ISRO
NavDR | Neural-Augmented DR

## Slide 2: IDEA TITLE
NavDR — AI-ML Intelligent Dead Reckoning for Seamless Navigation
PROBLEM
• GNSS fails in tunnels, parking garages and urban canyons → navigation freezes
• Pure IMU integration accumulates drift rapidly
SOLUTION
• TCN learns forward velocity from phone IMU → ESKF fuses motion → HMM constrains to OSM roads
• Target: <10% drift during GNSS denial • IO-VNBD benchmark + Indian-road validation
NAVIC-AWARE HANDOFF
NavIC-aware GNSS monitoring
C/N₀ degradation helps flag
obstruction / signal loss
Proactive transition before
generic outage thresholds
INTEGRITY MONITORING
Confidence ring from
ESKF covariance P
Radius reflects estimated
position uncertainty
Raw GNSS vs AI-DR
side-by-side demo
BAROMETRIC DETECTION
Pressure-rate tunnel detector
+ altitude constraint
Feature-flagged fallback
when barometer is absent
Stretch feature — not core
Phone IMU
100 Hz
Gravity
Alignment
TCN Speed
~50K params
ESKF+NHC
15-state
Map Match
HMM/Viterbi
Position
<10% drift

## Slide 3: TECHNICAL APPROACH
Python • PyTorch/ONNX Runtime • Android Kotlin • OSMDroid • Valhalla Meili • IO-VNBD
Phone IMU
Acc + Gyro @ 100 Hz
Raw MEMS data
Auto-Alignment
Gravity-based phone →
vehicle frame rotation
TCN / 1D-CNN
Forward velocity regression
~50K params
ESKF + NHC
15-state sensor fusion
Position, velocity, biases
HMM Map Match
Viterbi on offline OSM
Road-network constraint
NavIC GNSS
Proactive blackout trigger
Android GnssStatus API
NAVIC ADVANTAGE
NavIC-aware outage signal
C/N₀ trends support
proactive GNSS handoff
PRIOR WORK GAP
Vehicular smartphone DR
exists in literature
NavDR targets an
unmodified Android phone
DOMAIN ADAPTATION
Mounting-invariant inputs
Supplementary Indian-road
validation closes domain gap
Confidence ring: radius ∝ √(Pxx + Pyy)
ESKF covariance drives uncertainty UI

## Slide 4: FEASIBILITY AND VIABILITY
Real risks, concrete mitigations
RISK
MITIGATION
Android Doze mode can reduce IMU sampling
Foreground Service + partial WakeLock; verify sustained 100 Hz
Phone shifts / rotates on mount
Monitor alignment; recompute phone→vehicle rotation
IO-VNBD roads differ from India
Indian test-drive validation + augmentation / transfer learning
GNSS multipath gives a wrong but confident fix
Innovation / chi-square gating rejects inconsistent updates
ESKF math is the critical-path risk
Adapt open-source ESKF; fallback to simpler 2D KF

## Slide 5: IMPACT AND BENEFITS
Smartphone-first dead reckoning — zero dedicated vehicle hardware
SAFETY
Continuous navigation through
tunnels & underpasses
Emergency vehicles retain
route awareness
STRATEGIC
NavIC-aware GNSS handoff
Builds resilience around
India's own navigation system
ECONOMIC
₹0 dedicated hardware
Scales through software
deployment
SOCIAL
Budget-phone friendly
Useful for delivery, taxi,
logistics and personal nav
Target: <10% positional drift
On-device inference: low latency
No OBD-II / dedicated hardware
USE CASES: highway tunnels • multi-level parking •
urban canyons • forest roads • GNSS-denied zones
USERS: emergency responders • logistics fleets •
ride-hailing • delivery • personal navigation

## Slide 6: RESEARCH AND REFERENCES
Research basis and reference work
[1] Onyekpe et al. — IO-VNBD benchmark dataset. Data in Brief (2021). DOI: 10.1016/j.dib.2021.106885
[2] Brossard et al. — AI-IMU Dead-Reckoning. IEEE T-IV (2020). DOI: 10.1109/TIV.2020.2980758
[3] Sirikonda et al. — Tightly Coupled NavIC + Low-Cost Sensors. IEEE Sensors J. (2024). DOI: 10.1109/JSEN.2024.3367927
[4] Jayanth et al. — EqNIO: Subequivariant Neural Inertial Odometry. ICLR (2025).
[5] Onyekpe et al. — R-WhONet: Transfer Learning for Vehicular Positioning. NCA (2025). DOI: 10.1007/s00521-024-10046-z
[6] Valhalla — Meili HMM Map Matching engine. Open-source implementation.
[7] Android GnssStatus / raw GNSS APIs — on-device GNSS signal monitoring.
[8] Groves / Solà — integrated navigation and error-state Kalman filter foundations.
Preliminary result (simulated baseline — to be replaced with an IO-VNBD-trained result per PS requirement):
Naive strapdown DR: 85.7% drift over 60s | NHC-constrained (proxy): 7.5% drift — meets SIH <10% target